Vectrex Development System '95
------------------------------

The Hardware
------------
The system basically consists of a ram chip, two eproms and a serial interface.
A counter is used to switch between 32k ram and the various eprom banks which 
have a size of 16k each. As the cartridge address area is limited to 32k,
the memory map looks as follows:

Counter 
Value       0-7                 8-15
------------------------------------
$0000-$1fff eprom bank 0-7 (*)  RAM
$2000-$37ff not used            RAM
$3800-$3bff counter strobe(**)  counter strobe  
$3c00-$3fff ACIA registers      ACIA registers 

(*)  minimum configuration is one 2764 eprom ->4k
     max config. two 27512 eproms ->128k
(**) each read/write access increases the counter by one

A serial cable (RS232) can be used to connect the devsys with any terminal.

The Software
------------
Currently a modified version of vmon (by Jeff Lavin) is used as bootstrap.
It allows you to examine memory/registers and to download hexcode on the 
development system ram. The sourcecode has been modified for assembling with
the as09-package.
Future versions will (hopefully) feature a nice 3d-menu allowing
to choose between boot-monitor, rom-programs and minestorm.
 
The Layout
----------
I actually made a layout for the devsys, but it turned out to have some bugs  
which I had to correct manually during testing. If there are some people
interested, I will consider to release a corrected version.


Useful Hints
------------
- try checking ALL solder bridges, even if they look allright
- remember to CROSSconnect the RS232 handshake lines 


Instructions
------------
The following commands are usable for the boot monitor:

m	Memory exam (read/write)	
g	Go (set Program Counter)				
r	Register exam			
v	Verify Memory 			
t	Transfer file			
p	Protocol change 		

memory exam / modify 
--------------------
m <EA><CR>   -> '<CR><EA>,<CONTENTS>,'
	next expected inputs are:

a) HEX numbers ->these are stored as of <EA>, and the former 
	   	 contents are printed on screen.
b) '<' ('-')   -> go back 1 (16) Bytes
c) '+'         -> forward 16 Bytes 
d) '!<ASCII>   -> store <ASCII>+$80 in <EA> 
e) <ANY KEY>   -> show contents of next address
f) <CR>        -> end examine mode

<EA> = address (e.g. $4ac0)
<CR> = carriage return

'go' command 
------------
'g <EA>' -> go to <EA>
'g'      -> go to <PC> 

verify memory
-------------
no comment
(I didn't ever use this, so you'll have to find out for yourself...)

protocol change
---------------
'p:1'+<CR>	-> 2400  Baud
'p:2'+<CR>	-> 9600  Baud
'p:3'+<CR>	-> 19200 Baud

default setting is 9600 Baud

transfer file to vectrex
------------------------
't <EA>'+<CR> -> load to <EA>
't'+<CR>      -> load to $0000  
next expected inputs are (use your terminal program's 'ASCII UPLOAD'):

<hexbyte>-> is written to memory at current location
<CR>	   -> ends transfer

<hexbyte> = two-digit ASCII format number (e.g. 7f)

please note:

during transfer the vectrex screen is switched off
(software bug: my transfer protocol doesn't use RTS/CTS)

----------------------------------------------------------------

send comments & suggestions to: 

ub2f@rz.uni-karlsruhe.de (Ralph Kimmlingen)