VECTREX

PROGRAMMER’S

MANUAL

VOLUME  I

GENERAL INFORMATION

EXECUTIVE STOREAGE

UTILIZATION

REV	    DATE	PROG	COMMENT(S)

-	 MM/DD/YY	   JJH	   Initial Release

Vectrex Hardware Description	6

Vectrex Memory Map	6

6522 Interface Adapter	7

Register Access Map	7

Port ‘A’ / ‘B’ Direction Registers [DDAC & DCNTRL]	7

Port ‘A’ Data – DAC and PSG data [DAC]	7

Port ‘B’ Data – Vectrex Hardware Control [CNTRL]	8

Auxiliary Control Register [ACRTRL]	8

Peripheral Control Register [PCNTRL]	8

Port ‘A’ Handshake Controls (CA1 / 2)	8

Port ‘B’ Handshake Controls (CB1 / 2)	9

Timer #1	10

Timer #2	11

Shift Register [SHIFT]	12

Interrupt enable register [IENABL]	12

Interrupt flag register [IFLAG]	13

Programmable Sound Generator	14

Register Access Map	14

Tone / Noise Enables	14

Course / Fine Tone Period	14

Channel Amplitude	15

Noise Period	15

Envelope Period	15

Envelope Shape / Cycle	15

I/O Port	15

General executive description	16

Drawing format descriptions	16

‘Diffy’ Description	16

‘Duffy’ Description	16

‘Packet’ Description	16

Power-up / reset characteristics	16

Executive storage description	17

ABSX	17

ABSY	17

ACTPLY	17

ANGLE	17

BACON	18

B1FREQ	18

B2FREQ	18

DASH	19

DOREMI	19

DWELL	19

EDGE (HEDGES)	20

EPOT0 (DPOT0)	20

EPOT1 (DPOT1)	20

EPOT2 (DPOT2)	21

EPOT3 (DPOT3)	21

ETMP1	21

ETMP2	22

ETMP3	22

ETMP4	22

ETMP5	22

ETMP6	23

ETMP7	23

ETMP8	23

ETMP9	23

ETMP10	24

FADE	24

FADEA	24

FADEB	25

FADEC	25

FEAST	25

FRAME	26

FRMTIM (XMSEC)	26

F1FREQ	26

GAP	27

HISCOR (HEIGH)	27

KEY0	27

KEY1	27

KEY2	28

KEY3	28

KEY4	28

KEY5	29

KEY6	29

KEY7	29

K1FREQ	30

LAG	30

LASRAM	30

LATUS	30

LEG	31

LIST	31

MESAGE	32

NEDGE	32

NEWGEN	32

OPTION (GAMZ)	33

PEDGE	33

PLAYRS (PLAYRZ)	33

POT0	33

POT1	34

POT2	34

POT3	34

POTRES	35

RAMMES	35

RANCID	35

RATEA	35

RATEB	36

RATEC	36

REG0	36

REG1	37

REG2	37

REG3	37

REG4	37

REG5	38

REG6	38

REG7	38

REG8	39

REG9	39

REGA	39

REGB	39

REGC	40

REGD	40

REGE	40

REQ0	41

REQ1	41

REQ2	41

REQ3	42

REQ4	42

REQ5	43

REQ6	43

REQ7	44

REQ8	44

REQ9	44

REQA	45

REQB	45

REQC	46

REQD	46

RESTC	46

SATUS	47

SBTN	47

SCOR1	47

SCOR2	48

SEED	48

SIZRAS	48

SJOY	49

SPEKT	49

TENSTY	49

TEMP1	49

TEMP2	50

TEMP3	50

TEMP4	50

TEMP5	50

TEMP6	51

TEMP7	51

TEMP8	51

TEMP9	51

TEMP10	52

TMR1	52

TMR2	52

TMR3	52

TMR4	53

TONEA	53

TONEB	53

TONEC	54

TRIGGR	54

TSTAT	54

TUNE	55

VIBA	55

VIBB	55

VIBC	56

VIBE	56

WCSINE (COSINE)	56

WSINE (SINE)	57

XACON	57

XATUS	58

XTMR0 (X0)	58

XTMR1 (X1)	58

XTMR2 (X2)	58

XTMR3 (X3)	59

XTMR4 (X4)	59

XTMR5 (X5)	59

ZSKIP (ZGO)	60

Condensed Executive Parameter Requirements	61

Ram And Function Classifications	65

# Vectrex Hardware Description

The Vectrex consists of a 6809 microprocessor, 1k x 8 RAM, 8k x 8 resident ROM, 6522 interface adapter, D / A converter (+2.5 to –2.5 volts), 3 sample / holds (active ground, ‘Z’ and ‘Y’ axises), a programmable sound generator and 2 player controllers (one joystick and 4 buttons each).

The ROM contains the resident game ‘Mine Storm’ and the Executive.  The Executive consists of power-up / reset handler and a large selection of subroutines for drawing, calculation, game logic and / or hardware maintenance.

The 6522 interface adapter provides all the interface necessary between the microprocessor and the analog electronics (joysticks, D / A converter, sample / holds and programmable sound generator).  The interface adapter provides two 8-bit parallel ports, two 16-bit counters (timers) and an 8-bit shift register.

The 6522’s shift register is used by the dashing and raster drawing routines.

## Vectrex Memory Map

Address Range		Description

$000 - $7FFF		Open for game ROM

$DXX0 – $DXXF	Vectrex control registers (6522)

$E000 - $EFFF		Mine storm

$F000 - $FFFF		Executive

# 6522 Interface Adapter

## Register Access Map

Addr		Description

$D000		8-bit port ‘B’ (Control bits) [CNTRL]

$D001		8-bit port ‘A’ (DAC and PSC data) [DAC]

$D002		Port ‘B’ direction control [DCNTRL]

$D003		Port ‘A’ direction control [DDAC]

$D004-7		Timer #1 [T1LOLC, T1HOC, T1LOL, T1HOL]

$D008-9		Timer #2 [T2LOLC, T2HOC]

$D00A		Shift register [SHIFT]

$D00B		Auxiliary control register [ACNTRL]

$D00C		Peripheral control register [PCNTRL]

$D00D		Interrupt flag register [IFLAG]

$D00E		Interrupt enable register [IENABL]

$D00F		ORA

## Port ‘A’ / ‘B’ Direction Registers [DDAC & DCNTRL]

The ‘A’ direction register [DDAC] controls the direction of data flow for the ‘A’ data port [DAC].

The ‘B’ direction register [DCNTRL] controls the direction of data flow for the ‘B’ data port [CNTRL].

Data flow direction is determined on a bit-by-bit basis.  A 0 in a bit of the data direction register causes the corresponding data port pin to act as an input. A 1 causes the pin to act as an output.

## Port ‘A’ Data – DAC and PSG data [DAC]

When outputting data to the DAC, the data byte place in the port ‘A’ data register is in a two’s complement format (bit 6 of the data byte is the high order bit with bit 0 being the lowest.  Bit 7 of the data byte is used for the sign).  Therefore, the minimum hex value to the DAC is $80; $00 is the center point and $7F is the maximum.

When passing data with the programmable sound generator, the data direction will have to be set according to the type of transfer.

## Port ‘B’ Data – Vectrex Hardware Control [CNTRL]

Bit		Description

- Sample / Hold strobe

- Analog multiplexer select, bit 0

- Analog multiplexer select, bit 1

- Sound generator, term ‘BC1’

- Sound generator, term ‘DBIR’

- Analog compare term (Input to 6522)

- .

- Integrator ramp

## Auxiliary Control Register [ACRTRL]

Bit		Description

- Refer to Port ‘A’ description

- Refer to Port ‘B’ description

4-2		Refer to Shift register description

5		Refer to Timer #2 description

7-6		Refer to Timer #1 description

## Peripheral Control Register [PCNTRL]

Bit		Description

3-0		Refer to Port ‘A’ handshake controls

7-4		Refer to Port ‘B’ handshake controls

## Port ‘A’ Handshake Controls (CA1 / 2)

PCNTRL

Bit 0		Description

- The CA1 interupt flag (IFR1) will be set on a negative transition of the CA1 input pin.

- The CA1 interrupt flag (IFR1) will be set on a positive transition of the CA1 input pin.

The CA1 interrupt flag (IFR1) will be cleared on a read or write of the Port ‘A’ data register.

PCNTRL bits

3 2 1		Description

0 0 0	Interrupt input mode – Set CA2 interrupt flag (IFR0) on a negative transition of the CA2 input pin.  Clear the interrupt flag (IFR0) on a read or write of the Port ‘A’ data register.

0 0 1	Independent interrupt input mode – Set CA2 interrupt flag (IFR0) on a negative transition of the CA2 input pin.  Reading or writing of the Port ‘A’ data register does not affect the status of the interrupt flag (IFR0).

0 1 0	Interrupt input mode – Set CA2 interrupt flag (IFR0) on a positive transition of the CA2 input pin.  Clear the interrupt flag (IFR0) on a read or write of the Port ‘A’ data register.

0 1 1	Independent interrupt input mode – Set CA2 interrupt flag (IFR0) on a positive transition of the CA2 input pin.  Reading or writing of the Port ‘A’ data register does not affect the status of the interrupt flag (IFR0).

1 0 0	Handshake output mode – Set CA2 output pin low on a read or write of the Port ‘A’ data register.  Reset CA2 pin to high with an active transition of the CA1 input pin.

1 0 1	Pulse output mode – CA2 goes low for one cycle following a read or write of the Port ‘A’ data register.

1 1 0		Manual output mode – The CA2 output is held low in this mode.

1 1 1		Manual output mode – The CA2 output is held high in this mode.

## Port ‘B’ Handshake Controls (CB1 / 2)

PCNTRL

Bit 4		Description

0	The CB1 interrupt flag (IFR4) will be set on a negative transition of the CB1 input pin.

1	The CB1 interrupt flag (IFR4) will be set on a positive transition of the CB1 input pin.

The CA1 interrupt flag (IFR1) will be cleared on a read or write of the Port ‘A’ data register.

PCNTRL bits

7 6 5		Description

0 0 0	Interrupt input mode – Set CB2 interrupt flag (IFR3) on a negative transition of the CB2 input pin.  Clear the interrupt flag (IFR3) on a read or write of the Port ‘B’ data register.

0 0 1	Independent interrupt input mode – Set CB2 interrupt flag (IFR3) on a negative transition of the CB2 input pin.  Reading or writing of the Port ‘B’ data register does not affect the status of the interrupt flag (IFR3).

0 1 0	Interrupt input mode – Set CB2 interrupt flag (IFR3) on a positive transition of the CB2 input pin.  Clear the interrupt flag (IFR3) on a read or write of the Port ‘B’ data register.

0 1 1	Independent interrupt input mode – Set CB2 interrupt flag (IFR3) on a positive transition of the CB2 input pin.  Reading or writing of the Port ‘B’ data register does not affect the status of the interrupt flag (IFR3).

1 0 0	Handshake output mode – Set CB2 output pin low on a read or write of the Port ‘B’ data register.  Reset CB2 pin to high with an active transition of the CB1 input pin.

1 0 1	Pulse output mode – CB2 goes low for one cycle following a read or write of the Port ‘B’ data register.

1 1 0		Manual output mode – The CB2 output is held low in this mode.

1 1 1		Manual output mode – The CB2 output is held high in this mode.

## Timer #1

Addr		Label		Description

$D004		T1LOLC	Write into low order latch

Read from low-order counter and reset interrupt

$D005		T1HOC		Write into high-order latch, transfer latches to

counter and reset interrupt

Read from high-order counter

$D006		T1LOL		Write into low-order latch

Read from low-order latch

$D007		T1HOL		Write into high-order latch and reset timer #1 interrupt

Read from high-order latch

ACNTRL bits

7 6 			Description

0 0	Generate a single time-out interrupt each time timer #1 is loaded.  Output pin PB7 is disabled.

0 1	Generate continuous interrupts.  Output pin PB7 is disabled.

1 0	Generate a single interrupt and an output pulse on pin PB7 for timer #1 load operation.

1 1	Generate continuous interrupts and a square wave output on pin PB7.

#### One-shot Mode

The one-shot mode allows generation of a single interrupt each time a load operation occurs.  In addition to generating a single interrupt, Timer #1 can be programmed to produce a single negative pulse on the PB7 peripheral pin.  With the output enabled (ACNTRL7 = 1), a write to location $D005 [T1HOC] will cause PB7 to go low.  PB7 will return high when Timer #a counts down to zero.  For PB7 to act as the output of Timer #1, both the direction register for Port ‘B’ (bit 7) and the auxiliary control register (bit 7) must be set (e.g. – DCNTRL7 = 1 and ACNTRL7 = 1).

It is necessary to assure that the low order latch contains the proper data before initiating the count-down by writing to location $D005 [T1HOC].  When starting the down-count, the interrupt flag is cleared, the contents of the low-order latch will be transferred into the low-order counter and the timer will begin to decrement at the system clock rate.  If the PB7 output is enabled, this signal will go low on the phase two following the write operation.

When the counter reaches zero, the timer #1 interrupt flag will be set, the IRQ pin will go low and the signal on PB7 will go high.  The counter will still continue to decrement, this will allow the time since the interrupt to be determined (note: the timer #1 interrupt will not be set again unless it has previously cleared).

##### Free-running Mode

The most important advantages associated with the latches are the ability to produce a continuous series of evenly spaced interrupts and the ability to produce a square wave on PB7 whose frequency is not affected by variations in the processor interrupt response time.

In the free-running mode (ACNTRL6 = 1), the interrupt flag is set and the signal on PB7 is inverted each time the counter reaches zero.  However, instead of continuing to decrement from zero after a time-out, the timer automatically transfers the contents of the latch into the counter and continues to decrement from there.

## Timer #2

Addr		Label		Description

$D008		T1LOLC	Write into low order latch

Read from low-order counter and reset interrupt

$D009		T1HOC		Write into high-order latch, transfer latches to

counter and reset interrupt

Read from high-order counter

ACNTRL

Bit 5 			Description

0	.

1	.

#### Interval Timer Mode

In interval timer mode, Timer #2 operates in the ‘one-shot’ mode similar to timer #1.  Timer #2 issues an interrupt for each timer load operation.  After timing out, the counter will continue to decrement.

##### Pulse-counting Mode

In the pulse counting mode, Timer #2 serves primarily to count a predetermined number of negative transitions on PB6.  Writing into $D009 [T2HOC] clears the interrupt flag and allows the counter to decrement for each negative transition applied to PB6.  The interrupt flag will be set when Timer #2 reaches zero.

At this time the counter will continue to decrement with each negative transition on PB6.  The pulse must be low on the leading edge of phase two.

## Shift Register [SHIFT]

The shift register performs serial data transfers into and out of the CB2 pin under control of an internal modulo-8 counter.  Shift pulses can be applied to the CB1 pin from an external source or, with the proper mode selection, shift pulses generated internally will appear on the CB1 pin for controlling shifting in external devices.

The control bits which allow control of the various shift register operating modes are located in the Auxiliary control register [ACNTRL]:

ACNTRL bits

4 3 2			Descriptions

0 0 0			Shift register disabled

0 0 1			Shift-in under control of Timer #2

0 1 0			Shift-in at system clock rate

0 1 1			Shift-in under control of external pulses

1 0 0			Shift-out under control of Timer #2

1 0 1			Shift out under control of Timer #1

1 1 0			Shift out at system clock rate

1 1 1			Shift-out under control of external pulses

The data shifted-out of the shift register appears from bit 7 (note: at the same time, bit 7 is shifted-in at bit 0).

The first two shift-out modes differ in that the second mode (1 0 1) places the shift pulses on the CB1 pin.

The shift-in modes are not used with the standard Vectrex hardware and are described only for reference.

## Interrupt enable register [IENABL]

Enabling flags – When writing to the Interrupt enable register ($D00E) and bit 7 is set, then each 1 in bits 6 through 0 sets the corresponding bit in the Interrupt enable register.

Disabling flags – When writing to the Interrupt enable register ($D00E) and bit 7 is cleared, then each 1 in bits 6 through 0 clears the corresponding bit in the Interrupt enable register.

Bit	Description

- Enable / disable ‘CA2’ flag

- Enable / disable ‘CA1’ flag

- Enable / disable Shift register done flag

- Enable / disable ‘CB2’ flag

- Enable / disable ‘CB1’ flag

- Enable / disable Timer #2 flag

- Enable / disable Timer #1 flag

- Set / clear control

## Interrupt flag register [IFLAG]

Bit	Description

- Set by an active transition of ‘CA2’ signal

Cleared by the reading or writing of the Port ‘A’ data register (register address $D001).  Reading or writing the Port ‘A’ data at register address $D00F does not affect the setting of this bit.

- Set by an active transition of ‘CA1’ signal

Cleared by the reading or writing of the Port ‘A’ data register (register address $D001).  Reading or wriging the Port ‘A’ data at register address $D00F does not affect the setting of this bit.

- Shift register done

Cleared by the reading or writing of the shift register (register address $D00A).

- Set by an active transition of ‘CB2’ signal

Cleared by the reading or writing of the Port ‘B’ data register (register address $D000).

- Set by an active transition of ‘CB1’ signal

Cleared by the reading or writing of the Port ‘B’ data register (register address $D000).

- Timer #2 has down-counted to zero

Cleared by reading Timer #2’s low-order counter (register address $D008) or writing Timer #2’s high-order counter (register address $D009).

- Timer #1 has down-counted to zero

Cleared by reading Timer #1’s low-order counter (register address $D004) or writing Timer #1’s high-order counter (register address $D005).

- Logic expression of (IFR6 and IER6) or (IFR5 and IER5) or (IFR4 and IER4) or (IFR3 and IER3) or (IFR2 and IER2) or (IFR1 and IER1) or (IFR0 and IER0)

# Programmable Sound Generator

## Register Access Map

Reg	Description

$00	Channel A: Fine tone period

$01	Channel A: Course tone period

$02	Channel B: Fine tone period

$03	Channel B: Course tone period

$04	Channel C: Fine tone period

$05	Channel C: Course tone period

$06	Noise period

$07	Tone / Noise enables

$08	Channel A: Amplitude

$09	Channel B: Amplitude

$0A	Channel C: Amplitude

$0B	Fine envelope period

$0C	Course envelope period

$0D	Envelope shape / cycle

$0E	I/O Port

## Tone / Noise Enables

<This area was empty>

## Course / Fine Tone Period

The frequency of each square wave generated by the three Tone generators is obtained in the PSG by first counting down the input clock by 16, then by further counting down the result by the programmed 12-bit tone period value.  The 12-bit tone period is formed by the lower 4-bits of the course tone period (the upper 4-bits of the course tone period are not used) and the full byte of the fine tone period.

Note that the 12-bit value programmed in the combined course and fine tone registers is a ‘period’ value – the higher the value in the registers, the lower the resultant tone frequency.  (The lowest period value is $001).

## Channel Amplitude

The amplitudes of the signals generated by the three D/A converters (one for each channel) is determined by the contents of the lower 5 bits (B4 – B0) of register $08, $09 and $0A.

The amplitude mode (bit 4) selects either fixed level amplitude (M = 0) or variable level amplitude (M = 1).  It follows then that bit 3 thru 0 are only active when M = 0.  When fixed level amplitude is selected, it is ‘fixed’ only in the sense that the amplitude level is under the direct control of the system processor.  Varying the amplitude when in this ‘fixed’ amplitude mode requires in each instance the direct intervention of the system processor via an address latch / write data sequence to modify the amplitude setting.

When M = 1, the amplitude of each channel is determined by the envelope pattern as defined by the envelope generator’s 4-bit output.  The amplitude mode (bit ‘M’) should be thought of as an envelope enable bit.

## Noise Period

The frequency of the noise source is obtained in the PSG by first counting down the input clock by 16, then by further counting down the result by the programmed 5-bit noise period value.  This 5-bit value consists of the lower 5 bits of register $06.

Note that the 5-bit value in register $06 is a period value – the higher the value in the register, the lower the resultant noise frequency (the lowest period is $01).

## Envelope Period

The frequency of the envelope is obtained in the PSG by first counting down the input clock by 256, then by further counting down the result by the programmed 16-bit envelope period value.  This 16-bit value is formed by the course and fine envelope period registers.  Note that the 16-bit value formed by the course and fine envelope period registers is a period value – the higher the value in the registers, the lower the resultant envelope frequency (the lowest period is $0001).

## Envelope Shape / Cycle

<This area was empty>

## I/O Port

<This area was empty>

# General executive description

## Drawing format descriptions

### ‘Diffy’ Description

<This area was empty>

### ‘Duffy’ Description

<This area was empty>

### ‘Packet’ Description

<This area was empty>

## Power-up / reset characteristics

<This area was empty>

# Executive storage description

## ABSX

Location:	$C835

Description:

Working storage for ‘CMPASS’

Modified by:

CLREX, CMPASS

INTALL, INTMSC

## ABSY

Location:	$C834

Description:

Working storage for ‘CMPASS’

Modified by:

CLREX, CMPASS

INTALL, INTMSC

## ACTPLY

Location:	$C89B

Description:

Mine Storm: Currently active player ($00 or $02)

Modified by:

CLREX

Accessed by:

SCRMES

WAIT

## ANGLE

Location:	$C836

Description:

Location for parameter passing

Modified by:

CLREX, CMPASS

DROT

INTALL, INTMSC

LNROT, LROT90

MLTY8, MLTY16

PROT

Accessed by:

ADROT, ALNROT, APROT

BDROT

SINCOS

## BACON

Location:	$C876

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## B1FREQ

Location:	$C86B - $C86C (2 bytes)

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## B2FREQ

Location:	$C86D - $C86E (2 bytes)

Description:

Allocated but not used by Mine Store or Executive

Modified by:

CLREX

INTALL, INTMSC

## DASH

Location:	$C829

Description:

Dash pattern for drawing routines

Modified by:

CLREX

INTALL, INTMSC

Accessed by:

DASHDF, DASHPK, DSHDF, DSHDF1

## DOREMI

Location:	$C84D - $C84E (2 bytes)

Description:

Note table pointer

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

SPLAY

Accessed by:

REPLAY

TPLAY

## DWELL

Location:	$C828

Description:

Dot ‘ON’ time

Modified by:

CLREX

DOTTIM

INTALL, INTMSC

Accessed by:

ADOT

DDOT, DIFDOT, DOT, DOTAB, DOTPCK, DOTX

## EDGE (HEDGES)

Location:	$C811

Description:

xxxxxx

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## EPOT0 (DPOT0)

Location:	$C81F

Description:

Controller #1: Right / left joystick pot enable (must be $00 or $01)

Modified by:

CLREX

INTALL, INTMSC

WAIT

Accessed by:

JOYBIT, JOYSTK

## EPOT1 (DPOT1)

Location:	$C820

Description:

Controller #1: Up / down joystick pot enable (must be $00 or $03)

Modified by:

CLREX

INTALL, INTMSC

WAIT

Accessed by:

JOYBIT, JOYSTK

## EPOT2 (DPOT2)

Location:	$C821

Description:

Controller #2: Right / left joystick #2 enable (must be $00 or $05)

Modified by:

CLREX

INTALL, INTMSC

WAIT

Accessed by:

JOYBIT, JOYSTK

## EPOT3 (DPOT3)

Location:	$C822

Description:

Controller #2: Up / down joystick #2 enable (must be $00 or $07)

Modified by:

CLREX

INTALL, INTMSC

WAIT

Accessed by:

JOYBIT, JOYSTK

## ETMP1

Location:	$C883

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP2

Location:	$C884

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP3

Location:	$C885

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP4

Location:	$C886

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP5

Location:	$C887

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP6

Location:	$C888

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP7

Location:	$C889

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP8

Location:	$C88A

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP9

Location:	$C88B

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## ETMP10

Location:	$C88c – C88E (3 bytes)

Description:

Mine Storm: Temporary working storage

The last two bytes ($C88D - $C88E) serve as a guard against the sloppy programmer and are not used by existing software.

Modified by:

CLREX

## FADE

Location:	$C84F - $C850 (2 bytes)

Description:

Working storage for ‘SELOPT’ and tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

REPLAY

SELOPT, SPLAY

TPLAY

Accessed by:

XPLAY

## FADEA

Location:	$C85E

Description:

Working storage for ‘SELOPT’ and tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

REPLAY

SELOPT, SPLAY

TPLAY

Accessed by:

XPLAY

## FADEB

Location:	$C85F

Description:

Working storage for ‘SELOPT’ and tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

REPLAY

SELOPT, SPLAY

TPLAY

Accessed by:

XPLAY

## FADEC

Location:	$C860

Description:

Working storage for ‘SELOPT’ and tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

REPLAY

SELOPT, SPLAY

TPLAY

Accessed by:

XPLAY

## FEAST

Location:	$C871

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## FRAME

Location:	$C825 - $C826 (2 bytes)

Description:

Frame counter

Modified by:

CLREX

FRWAIT

INTALL, INTMSC

SELOPT

WAIT

## FRMTIM (XMSEC)

Location:	$C83D – C83E (2 bytes)

Description:

Frame rate

Modified by:

CLREX

INTALL, INTMSC

Accessed by:

FRWAIT

INTALL, INTPIA

SELOPT

WAIT

## F1FREQ

Location:	$C86F - $C870 (2 bytes)

Description:

Allocated but not used by Mine Store or Executive

Modified by:

CLREX

INTALL, INTMSC

## GAP

Location:	$C86A

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## HISCOR (HEIGH)

Location:	$C8EB - $C8F1 (7 bytes)

Description:

Contains ASCII high score

## KEY0

Location:	$C812

Description:

Controller #1 – Key #1: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## KEY1

Location:	$C813

Description:

Controller #1 – Key #2: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## KEY2

Location:	$C814

Description:

Controller #1 – Key #3: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## KEY3

Location:	$C815

Description:

Controller #1 – Key #4: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## KEY4

Location:	$C816

Description:

Controller #2 – Key #1: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## KEY5

Location:	$C817

Description:

Controller #2 – Key #2: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## KEY6

Location:	$C818

Description:

Controller #2 – Key #3: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## KEY7

Location:	$C819

Description:

Controller #2 – Key #4: De-bounced key depressed flag

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## K1FREQ

Location:	$C874 – $C875 (2 bytes)

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## LAG

Location:	$C83C

Description:

xxxxxx

Modified by:

ADROT, ALNROT, APROT

BDROT

CLREX

DROT

INTALL, INTMSC

LCSINE, LNROT, LROT90, LSINE

MCSINE, MLTY8, MLTY16, MSINE

PROT

SELOPT

## LASRAM

Location:	$C880

Description:

xxxxxx

## LATUS

Location:	$C868

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## LEG

Location:	$C83B

Description:

xxxxxx

Modified by:

ADROT, ALNROT, APROT

BDROT

CLREX

DROT

INTALL, INTMSC

LNROT, LROT90

MCSINE, MLTY8, MLTY16, MSINE

PROT

Accessed by:

LCSINE, LSINE

## LIST

Location:	$C823

Description:

Number of vectors to be drawn

Modified by:

ADROT, APROT

BDROT, BYTADD

CLREX

DASHDF, DASHPK, DIFDOT, DIFFAB, DIFFAX, DIFFY, DIFLST, DIFTIM, DROT, DSHDF, DSHDF1, DUFFAB, DUFFAX, DUFFY, DUFLST, DUFTIM

INTALL, INTMSC

JOYBIT, JOYSTK

LDIFFY, LDUFFY

PROT

SCRADD, SELOPT, STKADD

TDIFFY, TDUFFY

WAIT

## MESAGE

Location:	$C82C - $C82D (2 bytes)

Description:

xxxxxx

Modified by:

ASMESS

CLREX

DSHIP

INTALL, INTMSC

MSSPOS

RASTER, RSTPOS, RSTSIZ

SCRBTH, SCRMES, SELOPT, SHIPX, SMESS

TXTPOS, TXTSIZ

WAIT

Accessed by:

MRASTR

## NEDGE

Location:	$C873

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## NEWGEN

Location:	$C855

Description:

Working storage for tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

REPLAY

SPLAY

TPLAY

## OPTION (GAMZ)

Location:	$C87A

Description:

Number of player options ($01 - $09)

Modified by:

CLREX

INTALL, INTMSC

SELOPT

## PEDGE

Location:	$C872

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## PLAYRS (PLAYRZ)

Location:	$C879

Description:

Number of players ($01 - $09)

Modified by:

CLREX

INTALL, INTMSC

SELOPT

Accessed by:

SCRBTH

## POT0

Location:	$C81B

Description:

Controller #1: Right / left joystick pot value

Modified by:

CLREX

INTALL, INTMSC

JOYBIT, JOYSTK

WAIT

## POT1

Location:	$C81C

Description:

Controller #1: Up / down joystick pot value

Modified by:

CLREX

INTALL, INTMSC

JOYBIT, JOYSTK

WAIT

## POT2

Location:	$C81D

Description:

Controller #2: Right / left joystick pot value

Modified by:

CLREX

INTALL, INTMSC

JOYBIT, JOYSTK

WAIT

## POT3

Location:	$C81E

Description:

Controller #2: Up / down joystick pot value

Modified by:

CLREX

INTALL, INTMSC

JOYBIT, JOYSTK

WAIT

## POTRES

Location:	$C81A

Description:

Joystick resolution limit

Modified by:

CLREX

INTALL, INTMSC

Accessed by:

JOYBIT, JOYSTK

WAIT

## RAMMES

Location:	$CA00

Description:

xxxxxx

## RANCID

Location:	$C87D – C87F (3 bytes)

Description:

Working storage for random number generators

Modified by:

CLREX, CONE

INTALL, INTMSC

RAND3, RANDOM, RANPOS

## RATEA

Location:	$C858

Description:

Working storage for ‘EXPLOD’

Modified by:

CLREX

EXPLOD

INTALL, INTMSC

## RATEB

Location:	$C85A

Description:

Working storage for ‘EXPLOD’

Modified by:

CLREX

EXPLOD

INTALL, INTMSC

## RATEC

Location:	$C85C

Description:

Working storage for ‘EXPLOD’

Modified by:

CLREX

EXPLOD

INTALL, INTMSC

## REG0

Location:	$C800

Description:

Channel A: Fine tone period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG1

Location:	$C801

Description:

Channel A: Course tone period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG2

Location:	$C802

Description:

Channel B: Fine tone period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG3

Location:	$C803

Description:

Channel B: Course tone period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG4

Location:	$C804

Description:

Channel C: Fine tone period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG5

Location:	$C805

Description:

Channel C: Course tone period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG6

Location:	$C806

Description:

Noise period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG7

Location:	$C807

Description:

Tone / Noise enables

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG8

Location:	$C808

Description:

Channel A: Amplitude

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REG9

Location:	$C809

Description:

Channel B: Amplitude

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REGA

Location:	$C80A

Description:

Channel C: Amplitude

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REGB

Location:	$C80B

Description:

Fine envelope period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REGC

Location:	$C80C

Description:

Course envelope period

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REGD

Location:	$C80D

Description:

Envelope shape / cycle

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REGE

Location:	$C80E

Description:

I/O port data register

Modified by:

CLREX

INTALL, INTMSC, INTPSG

REQOUT

WRREG

## REQ0

Location:	$C83F

Description:

Envelope shape / cycle

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ1

Location:	$C840

Description:

Course envelope period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ2

Location:	$C841

Description:

Fine envelope period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ3

Location:	$C842

Description:

Channel C: Amplitude

Modified by:

ASPLAY
CLREX

EXPLOD

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SETAMP, SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ4

Location:	$C843

Description:

Channel B: Amplitude

Modified by:

ASPLAY

CLREX

EXPLOD

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SETAMP, SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ5

Location:	$C844

Description:

Channel A: Amplitude

Modified by:

ASPLAY

CLREX

EXPLOD

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SETAMP, SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ6

Location:	$C845

Description:

Tone / noise enables

Modified by:

ASPLAY

CLREX

EXPLOD

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ7

Location:	$C846

Description:

Noise period

Modified by:

ASPLAY

CLREX

EXPLOD

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ8

Location:	$C847

Description:

Channel C: Course tone period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQ9

Location:	$C848

Description:

Channel C: Fine tone period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQA

Location:	$C849

Description:

Channel B: Course tone period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQB

Location:	$C84A

Description:

Channel B: Fine tone period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQC

Location:	$C84B

Description:

Channel A: Course tone period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## REQD

Location:	$C84C

Description:

Channel A: Fine tone period

Modified by:

ASPLAY

CLREX

INTALL, INTMSC, INTPSG, INTREQ

REPLAY

SPLAY

TPLAY

XPLAY

Accessed by:

REQOUT

## RESTC

Location:	$C857

Description:

Working storage for tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

REPLAY

SPLAY

TPLAY

XPLAY

## SATUS

Location:	$C867

Description:

Working storage for ‘EXPLOD’

Modified by:

CLREX

EXPLOD

INTALL, INTMSC

## SBTN

Location:	$C880

Description:

xxxxxx

Modified by:

CLREX

Accessed by:

WAIT

## SCOR1

Location:	$C8A8 - $C8AE (7 bytes)

Description:

xxxxxx

Modified by:

CLREX

## SCOR2

Location:	$C8AF – C8B5 (7 bytes)

Description:

xxxxxx

Modified by:

CLREX

## SEED

Location:	$C87B - $C87C (2 bytes)

Description:

xxxxxx

Modified by:

CLREX

INTALL, INTMSC

## SIZRAS

Location:	$C82A - $C82B (2 bytes)

Description:

xxxxxx

Modified by:

CLREX

INTALL, INTMSC

RSTSIZ

SCRBTH, SCRMES, SELOPT, SMESS

WAIT

Accessed by:

ASMESS

DSHIP

MRASTR, MSSPOS

RASTER, RSTPOS

SHIPX

TXTPOS

## SJOY

Location:	$C881

Description:

xxxxxx

Modified by:

CLREX

Accessed by:

WAIT

## SPEKT

Location:	$C878

Description:

Allocated but not used by Mine Store or Executive

Modified by:

CLREX

INTALL, INTMSC

## TENSTY

Location:	$C827

Description:

Contains the last value used for the intensity setting

Modified by:

CLREX

INT1Q, INT2Q, INT3Q, INTALL, INTENS, INTMAX, INTMSC

SCRBTH, SCRMES, SELOPT

WAIT

## TEMP1

Location:	$C88F

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP2

Location:	$C890

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP3

Location:	$C891

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP4

Location:	$C892

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP5

Location:	$C893

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP6

Location:	$C894

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP7

Location:	$C895

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP8

Location:	$C896

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP9

Location:	$C897

Description:

Mine Storm: Temporary working storage

Modified by:

CLREX

## TEMP10

Location:	$C898 - $C89A (3 bytes)

Description:

Mine Storm: Temporary working storage

The last two bytes *$C899 - $C89A) serve as a guard against the sloppy programmer and are not used by existing software.

Modified by:

CLREX

## TMR1

Location:	$C89C - $C89E (3 bytes)

Description:

xxxxxx

Modified by:

CLREX

WAIT

## TMR2

Location:	$C89F - $C8A1 (3 bytes)

Description:

xxxxxx

Modified by:

CLREX

WAIT

## TMR3

Location:	$C8A2 – C8A4 (3 bytes)

Description:

xxxxxx

Modified by:

CLREX

WAIT

## TMR4

Location:	$C8A5 - $ C8A7 (3 bytes)

Description:

xxxxxx

Modified by:

CLREX

WAIT

## TONEA

Location:	$C861 - $C862 (2 bytes)

Description:

Working storage for ‘SELOPT’ and tune player subroutines

Modified by:

CLREX

INTALL, INTMSC

SELOPT

Accessed by:

ASPLAY

REPLAY

SPLAY

TPLAY

XPLAY

## TONEB

Location:	$C863 - $C864 (2 bytes)

Description:

Working storage for ‘SELOPT’ and tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

SELOPT, SPLAY

TPLAY

Accessed by:

REPLAY

XPLAY

## TONEC

Location:	$C865 - $C866 (2 bytes)

Description:

Working storage for tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

SPLAY

TPLAY

Accessed by:

REPLAY

XPLAY

## TRIGGR

Location:	$C80F - $C810 (2 bytes)

Description:

Current controller button status. (‘TRIGGR + 1’ contains an image of ‘TRIGGR’ from the last time that the buttons were read).

Modified by:

CLREX

DBNCE

INPUT, INTALL, INTMSC

SELOPT

WAIT

## TSTAT

Location:	$C856

Description:

Working storage for tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

REPLAY

SPLAY

TPLAY

XPLAY

## TUNE

Location:	$C853 - $C854 (2 bytes)

Description:

xxxxxx

Modified by:

ASPLAY

CLREX

EXPLOD

INTALL, INTMSC

REPLAY

SPLAY

TPLAY

XPLAY

## VIBA

Location:	$C859

Description:

Working storage for ‘EXPLOD’

Modified by:

CLREX

EXPLOD

INTALL, INTMSC

## VIBB

Location:	$C85B

Description:

Working storage for ‘EXPLOD’

Modified by:

CLREX

EXPLOD

INTALL, INTMSC

## VIBC

Location:	$C85D

Description:

Working storage for ‘EXPLOD’

Modified by:

CLREX

EXPLOD

INTALL, INTMSC

Accessed by:

## VIBE

Location:	$C851

Description:

Working storage for tune player subroutines

Modified by:

ASPLAY

CLREX

INTALL, INTMSC

SPLAY

TPLAY

Accessed by:

REPLAY

## WCSINE (COSINE)

Location:	$C839 – C83A (2 bytes)

Description:

Location for parameter passing.  Generally contains the last cosine value calculated.

Modified by:

ADROT, ALNROT, APROT

BDROT

CLREX

DROT

INTALL, INTMSC

LNROT, LROT90

MLTY8, MLTY16

PROT

SINCOS

Accessed by:

LCSINE

MCSINE

## WSINE (SINE)

Location:	$C837 - $C838 (2 bytes)

Description:

Location for parameter passing.  Generally contains the last sine value calculated

Modified by:

ADROT, ALNROT, APROT

BDROT

CLREX

DROT

INTALL, INTMSC

LNROT, LROT90

MLTY8, MLTY16

PROT

SINCOS

Accessed by:

LSINE

MSINE

## XACON

Location:	$C877

Description:

Working storage for ‘EXPLOD’

Modified by:CLREX

EXPLOD

INTALL, INTMSC

## XATUS

Location:	$C869

Description:

Allocated but not used by Mine Storm or Executive

Modified by:

CLREX

INTALL, INTMSC

## XTMR0 (X0)

Location:	$C82E

Description:

xxxxxx

Modified by:

CLREX

D3TMR, DECTMR

INTALL, INTMSC

SELOPT

## XTMR1 (X1)

Location:	$C82F

Description:

xxxxxx

Modified by:

CLREX

D3TMR, DECTMR

INTALL, INTMSC

SELOPT

## XTMR2 (X2)

Location:	$C830

Description:

xxxxxx

Modified by:

CLREX

D3TMR, DECTMR

INTALL, INTMSC

SELOPT

## XTMR3 (X3)

Location:	$C831

Description:

xxxxxx

Modified by:

CLREX

DECTMR

INTALL, INTMSC

## XTMR4 (X4)

Location:	$C832

Description:

xxxxxx

Modified by:

CLREX

DECTMR

INTALL, INTMSC

## XTMR5 (X5)

Location:	$C833

Description:

xxxxxx

Modified by:

CLREX

DECTMR

INTALL, INTMSC

## ZSKIP (ZGO)

Location:	$C824

Description:

xxxxxx

Modified by:

CLREX

INTALL, INTMSC

Accessed by:

APACK

CZERO

DASHDF, DASHPK, DIFFAB, DIFFAX, DIFFY, DIFLST, DIFTIM, DPACK, DSHDF, DSHDF1, DUFFAB, DUFFAX, DUFFY, DUFLST, DUFTIM

LDIFFY, LDUFFY, LPACK

PACK1X, PACK2X, PACKET

TDIFFY, TDUFFY, TPACK

# Condensed Executive Parameter Requirements

| Subroutine | Entry Values | Return Values |
| --- | --- | --- |
| ABSAB | A, B | A, B |
| ABSB | B | B |
| ACTGND | DP | A, B |
| ADOT | Y, DP, DWELL | Same as entry values |
| ADROT | X, U, ANGLE, LIST | A, B, X, U, LIST |
| ALNROT | A, DP, ANGLE | A, B |
| APACK | B, X, Y, DP, ZSKIP | Same as entry values |
| APROT | X, U, ANGLE | A, B, X, U, LIST |
| ASMESS | Y, U, DP, SIZRAS | Same as entry values |
| ASPLAY | X, U, DP | A, B, X, Y, U |
| BCLR | B, X | A, B |
| BDROT | B, X, U, ANGLE | A, B, X, U |
| BLKFIL | A, B, X | B |
| BLKMOV | A, X, U | A, B |
| BLKMV1 | A, X, U | A, B |
| BXTEST | A, B, X, Y | CC |
| BYTADD | A, X, LIST | A, B, U |
| CLRBLK | A, B, X | A, B |
| CLREX | None required | A, B, X |
| CLR80 | B, X | A, B |
| CLR256 | X | A, B |
| CMPASS | A, B, DP | A, B, ANGLE |
| CONE | SEED | B |
| COSINE | A | A, B, X |
| CZERO | DP, ZSKIP | A, B |
| D3TMR | None required | B, X |
| DASHDF | X, DP, DASH, LIST | A, B, X, LIST, T1LOLC, ZSKIP |
| DASHPK | X, DP, DASH, T1LOLC, ZSKIP | A, B, X, LIST |
| DBNCE | A, DP | A, B, X, EDGE, KEY0 – KEY7, TRIGGR, TRIGGR + 1 |
| DDOT | Y, DP, DWELL | Same as entry values |
| DECBIT | A | A, X |
| DECTMR | None required | B, X |
| DEFLOK | DP | A, B, X |
| DEL | B | B |
| DEL13 | None required | Same as entry values |
| DEL20 | None required | B |
| DEL28 | None required | B |
| DEL33 | None required | B |
| DEL38 | None required | B |
| DIFDOT | X, DP, DWELL, LIST, T1LOLC | A, B, X, LIST |
| DIFFAB | A, B, DP, LIST, T1LOLC, ZSKIP | A, B, X |
| DIFFAX | X, DP, T1LOLC, ZSKIP | A, B, X, LIST |
| DIFFY | X, DP, LIST, T1LOLC, ZSKIP | A, B, X, LIST |
| DIFLST | X, DP, ZSKIP | A, B, X, LIST |
| DIFTIM | B, X, DP, LIST, ZSKIP | A, B, X, LIST |
| DOT | DP, DWELL | A, B |
| DOTAB | A, B, DP, DWELL, T1LOLC | A, B |
| DOTPCK | X, DP, DWELL, T1LOLC | A, B, X |
| DOTTIM | B, X, DP, T1LOLC | A, B, X |
| DOTX | X, DP, DWELL, T1LOLC | A, B, X |
| DPACK | B, X, Y, DP | Same as entry values |
| DPIO | None required | A, DP |
| DPRAM | None required | A, DP |
| DROT | A, B, X, U | A, B, X, U, LIST |
| DSHDF | A, X, DP, DASH, T1LOLC, ZSKIP | A, B, X, LIST |
| DSHDF1 | A, X, DP, DASH, T1LOLC, ZSKIP | A, B, X, LIST |
| DSHIP | A, B, X, DP, SIZRAS | A, B, X, U |
| DUFFAB | A, B, DP, LIST, T1LOLC, ZSKIP | A, B, X |
| DUFFAX | X, DP, T1LOLC, ZSKIP | A, B, X, LIST |
| DUFFY | X, DP, LIST, T1LOLC, ZSKIP | A, B, X, LIST |
| DUFLST | X, DP, ZSKIP | A, B, X, LIST |
| DUFTIM | B, X, DP, ZSKIP | A, B, X, LIST |
| DZERO | None required | A, B, DP |
| EXPLOD | U, DP | A, B, X, XACON |
| FRWAIT | FRMTIM | A, B, X, DP` |
| HISCR | X, U | A, B, X, U |
| INPUT | DP | A, B, X |
| INT1Q | DP | A, B |
| INT2Q | DP | A, B |
| INT3Q | DP | A, B |
| INTALL | None required | A, B, X, DP |
| INTENS | A, DP | A, B |
| INTMAX | DP | A, B |
| INTMSC | None required | A, B, X, DP |
| INTPIA | FRMTIM | A, B, X, DP |
| INTPSG | DP | A, B, X |
| INTREQ | None required | A, B, X |
| JOYBIT | DP, EPOTx, LIST, POTRES | A, B, X, LIST, POTx |
| JOYSTK | DP, EPOTx, POTRES | A, B, X, LIST, POTx |
| LCSINE | DP, LEG, WCSINE | A, B |
| LDIFFY | A, X, DP, T1LOLC, ZSKIP | A, B, X, LIST |
| LDUFFY | A, X, DP, T1LOLC, ZSKIP | A, B, X, LIST |
| LNROT | A, B, DP | A, B |
| LPACK | X, DP, ZSKIP | A, B, X |
| LROT90 | A, B, DP | A, B |
| LSINE | DP, LEG, WSINE | A, B |
| MCSINE | A, DP, WCSINE | A, B, LEG |
| MLTY8 | A, B, DP | X, Y |
| MLTY16 | A, B, DP | X, Y |
| MRASTR | DP, MESAGE, SIZRAS | A, B, X, U` |
| MSINE | A, DP | A, B, LEG |
| MSSPOS | A, B, U, DP, SIZRAS | A, B, X, U |
| OFF1BX | A, B, X, Y, U | CC |
| OFF2BX | A, B, X, Y, U | CC |
| PACKET | X, DP, T1LOLC, ZSKIP | A, B, X |
| PACK1X | X, DP, ZSKIP | A, B, X |
| PACK2X | X, DP, ZSKIP | A, B, X |
| POSIT1 | X, DP | A, B, X |
| POSIT2 | X, DP | A, B, X |
| POSITB | B, X, DP | A, B, X |
| POSITD | A, B, DP | A, B |
| POSITN | A, B, DP, T1LOLC | A, B |
| POSITX | X, DP, T1LOLC | A, B, X |
| POSWID | X, DP | A, B |
| PROT | A, X, U | A, B, X, U, LIST |
| PSGLST | U, DP | A, B, X, U |
| PSGMIR | X, U, DP | A, B, U |
| RAND3 | SEED | A |
| RANDOM | SEED | A |
| RANPOS | SEED | A, B |
| RASTER | U, DP, SIZRAS | A, B, X, U |
| REQOUT | DP, REQ0 – REQD | A, B, X, U |
| REPLAY | U, DP | A, B, X, Y, U |
| RSTPOS | U, DP, SIZRAS | A, B, X, U |
| RSTSIZ | U, DP | A, B, X, U |
| SCLR | X | A, B |
| SCRADD | A, B, X, LIST | A, B |
| SCRBTH | DP, PLAYRS, SCOR1, SCOR2 | A, B, Y, U |
| SCRMES | DP, ACTPLY, SCOR1, SCOR2 | A, B, Y, U |
| SELOPT | A, B | PLAYRS, OPTION |
| SETAMP | B, DP | A, X |
| SHIPX | A, B, X, DP, SIZRAS | A, B, X, U |
| SINCOS | DP, ANGLE | A, B, WCSINE, WSINE |
| SINE | A | A, B, X |
| SMESS | U, DP | Same as entry values |
| SPLAY | U, DP | A, B, X, Y, U |
| STKADD | S, LIST | A, B, S |
| TDIFFY | A, B, X, DP, ZSKIP | A, B, X, LIST |
| TDUFFY | A, B, X, DP, ZSKIP | A, B, X, LIST |
| TIMER |  |  |
| TPACK | B, X, DP, ZSKIP | A, B, X |
| TPLAY | U, DP | A, B, X, Y, U |
| TXTPOS | U, DP, SIZRAS | A, B, X, U |
| TXTSIZ | U, DP | A, B, X, U |
| WAIT | None required |  |
| WINNER | X, U | A, B, X, U |
| WRPSG | A, B, X, DP | B |
| WRREG | A, B, DP | B, X |
| XPLAY | DP | A, B, X, TSTAT |
| ZERGND | DP | A, B |
| ZERO | DP | A, B |

# Ram And Function Classifications

ASPLAY, Working storage, FADE

ASPLAY, Working storage, FADEA

ASPLAY, Working storage, FADEB

ASPLAY, Working storage, FADEC

ASPLAY, Working storage, NEWGEN

ASPLAY, Working storage, RESTC

ASPLAY, Working storage, TONEA

ASPLAY, Working storage, TONEB

ASPLAY, Working storage, TONEC

ASPLAY, Working storage, TSTAT

ASPLAY, Working storage, VIBE

Absolute value ABSAB (ABSVAL)

Absolute value, ABSB (AOK)

Active-ground, ACTGND (ZEREF)

Active-ground, CZERO (ZEGO)

Active-ground, DEFLOK

Active-ground, DZERO (ZERO.DP)

Active-ground, FRWAIT (FRAM20)

Active-ground, WAIT

Active-ground, ZERGND (ZEROIT)

Active-ground, ZERO (ZERO.)

Arithmetic subroutines, General, ABSAB (ABSVAL)

Arithmetic subroutines, General, ABSB (AOK)

Arithmetic subroutines, General, DECBIT (BITE)

Arithmetic subroutines, Random number, CONE

Arithmetic subroutines, Random number, RAND3

Arithmetic subroutines, Random number, RANDOM

Arithmetic subroutines, Random number, RANPOS

Arithmetic subroutines, Raster Score, BYTADD (SHADD)

Arithmetic subroutines, Raster Score, HISCR (HIGHSCR)

Arithmetic subroutines, Raster Score, SCLR

Arithmetic subroutines, Raster Score, SCRADD (SADD)

Arithmetic subroutines, Raster Score, STKADD (SADD2)

Arithmetic subroutines, Raster Score, WINNER

Arithmetic subroutines, Rotation, DIFFY, ADROT (DIFROT)

Arithmetic subroutines, Rotation, DIFFY, BDROT (DISROT)

Arithmetic subroutines, Rotation, DIFFY, DROT (DANROT)

Arithmetic subroutines, Rotation, DUFFY, ADROT (DIFROT)

Arithmetic subroutines, Rotation, DUFFY, BDROT (DISROT)

Arithmetic subroutines, Rotation, DUFFY, DROT (DANROT)

Arithmetic subroutines, Rotation, LINE, ALNROT (ROTAR)

Arithmetic subroutines, Rotation, LINE, LNROT (ROTOR)

Arithmetic subroutines, Rotation, LINE, LROT90 (RATOR)

Arithmetic subroutines, Rotation, LINE, MLTY16

Arithmetic subroutines, Rotation, LINE, MLTY8

Arithmetic subroutines, Rotation, PACKET, APROT (POTATE)

Arithmetic subroutines, Rotation, PACKET, PROT (POTATA)

Arithmetic subroutines, Trigonometric, ALNROT (ROTAR)

Arithmetic subroutines, Trigonometric, CMPASS (COMPAS)

Arithmetic subroutines, Trigonometric, COSINE (COSGET)

Arithmetic subroutines, Trigonometric, LCSINE (RCOS)

Arithmetic subroutines, Trigonometric, LNROT (ROTOR)

Arithmetic subroutines, Trigonometric, LROT90 (RATOR)

Arithmetic subroutines, Trigonometric, LSINE (RSIN)

Arithmetic subroutines, Trigonometric, MCSINE (RCOSA)

Arithmetic subroutines, Trigonometric, MLTY16

Arithmetic subroutines, Trigonometric, MLTY8

Arithmetic subroutines, Trigonometric, MSINE (RSINA)

Arithmetic subroutines, Trigonometric, SINCOS

Arithmetic subroutines, Trigonometric, SINE (SINGET)

Block initialization, BCLR (CLRSOM)

Block initialization, BLKFIL (FILL)

Block initialization, CLR256

Block initialization, CLR80 (NEGSOM)

Block initialization, CLRBLK (GILL)

Block initialization, CLREX (CLRMEM)

Block transfer, BLKMOV (STFAUX)

Block transfer, BLKMV1 (BAGAUX)

Button related RAM, EDGE (HEDGES)

Button related RAM, KEY0

Button related RAM, KEY1

Button related RAM, KEY2

Button related RAM, KEY3

Button related RAM, KEY4

Button related RAM, KEY5

Button related RAM, KEY6

Button related RAM, KEY7

Button related RAM, SBTN

Button related RAM, TRIGGR

Button related subroutines, DBNCE (ENPUT)

Button related subroutines, INPUT

Button related subroutines, SELOPT (OPTION)

Button related subroutines, WAIT

CMPASS, Working Storage, ABSY

CMPASS, Working Storage, ABSX

CONE, Working storage, RANCID

Collision subroutines, BXTEST (FINEBOX)

Collision subroutines, OFF1BX (OFF1BOX)

Collision subroutines, OFF2BX (OFF2BOX)

Controller related RAM, EDGE (HEDGES)

Controller related RAM, EPOT0 (DPOT0)

Controller related RAM, EPOT1 (DPOT1)

Controller related RAM, EPOT2 (DPOT2)

Controller related RAM, EPOT3 (DPOT3)

Controller related RAM, KEY0

Controller related RAM, KEY1

Controller related RAM, KEY2

Controller related RAM, KEY3

Controller related RAM, KEY4

Controller related RAM, KEY5

Controller related RAM, KEY6

Controller related RAM, KEY7

Controller related RAM, POT0

Controller related RAM, POT1

Controller related RAM, POT2

Controller related RAM, POT3

Controller related RAM, POTRES

Controller related RAM, SBTN

Controller related RAM, SJOY

Controller related RAM, TRIGGR

Controller related subroutines, DBNCE (ENPUT)

Controller related subroutines, INPUT

Controller related subroutines, JOYBIT (PBANG4)

Controller related subroutines, JOYSTK (POTS4)

Controller related subroutines, WAIT

Cosine subroutines, COSINE (COSGET)

Cosine subroutines, LCSINE (RCOS)

Cosine subroutines, MCSINE (RCOSA)

Cosine subroutines, SINCOS

DASH format, DASHDF (DASHY)

DASH format, DASHPK (DASHY3)

DASH format, DSHDF (DASHEL)

DASH format, DSHDF1 (DASHE)

DIFFY format, ADROT (DIFROT)

DIFFY format, BDROT (DISROT)

DIFFY format, DASHDF (DASHY)

DIFFY format, DIFDOT

DIFFY format, DIFFAX

DIFFY format, DIFFY

DIFFY format, DIFLST (DIFFX)

DIFFY format, DIFTIM

DIFFY format, DROT (DANROT)

DIFFY format, DSHDF (DASHEL)

DIFFY format, DSHDF1 (DASHE)

DIFFY format, LDIFFY (DIFLST)

DIFFY format, TDIFFY (DIFTLS)

DOT format, ADOT

DOT format, DDOT

DOT format, DIFDOT

DOT format, DOT

DOT format, DOTAB

DOT format, DOTPCK (DOTPAK)

DOT format, DOTTIM

DOT format, DOTX

DUFFY format, ADROT (DIFROT)

DUFFY format, BDROT (DISROT)

DUFFY format, DIFDOT

DUFFY format, DROT (DANROT)

DUFFY format, DUFFAX

DUFFY format, DUFFY

DUFFY format, DUFLST

DUFFY format, DUFTIM

DUFFY format, LDUFFY (DUFLST)

DUFFY format, TDUFFY (DUFTLS)

Delay subroutines, DEL

Delay subroutines, DEL13

Delay subroutines, DEL20

Delay subroutines, DEL28,

Delay subroutines, DEL33

Delay subroutines, DEL38

Drawing formats, ‘Diffy’

Drawing formats, ‘Duffy’

Drawing formats, ‘Packet’

Drawing subroutines, DASHED, DIFFY format, DASHDF (DASHY)

Drawing subroutines, DASHED, DIFFY format, DSHDF (DASHEL)

Drawing subroutines, DASHED, DIFFY format, DSHDF1 (DASHE)

Drawing subroutines, DASHED, DUFFY format, DASHDF (DASHY)

Drawing subroutines, DASHED, DUFFY format, DSHDF (DASHEL)

Drawing subroutines, DASHED, DUFFY format, DSHDF1 (DASHE)

Drawing subroutines, DASHED, PACKET format, DASHPK (DASHY3)

Drawing subroutines, DIFFY DOT format, DIFDOT

Drawing subroutines, DIFFY DOT format, DOTTIM

Drawing subroutines, DIFFY DOT format, DOTX

Drawing subroutines, DIFFY format, DIFFAX

Drawing subroutines, DIFFY format, DIFFY

Drawing subroutines, DIFFY format, DIFLST (DIFFX)

Drawing subroutines, DIFFY format, DIFTIM

Drawing subroutines, DIFFY format, LDIFFY (DIFLST)

Drawing subroutines, DIFFY format, TDIFFY (DIFTLS)

Drawing subroutines, DOT format, ADOT

Drawing subroutines, DOT format, DDOT

Drawing subroutines, DOT format, DOT

Drawing subroutines, DOT format, DOTAB

Drawing subroutines, DUFFY format, DUFFAX

Drawing subroutines, DUFFY format, DUFFY

Drawing subroutines, DUFFY format, DUFLST (DUFFX)

Drawing subroutines, DUFFY format, DUFTIM

Drawing subroutines, DUFFY format, LDUFFY (DUFLST)

Drawing subroutines, DUFFY format, TDUFFY (DUFTLS)

Drawing subroutines, MARKER format, DSHIP (SHIPSHO)

Drawing subroutines, MARKER format, SHIPX (SHIPSAT)

Drawing subroutines, PACKET DOT format, DOTPCK (DOTPAK)

Drawing subroutines, PACKET format, APACK

Drawing subroutines, PACKET format, DPACK

Drawing subroutines, PACKET format, LPACK (PACXX)

Drawing subroutines, PACKET format, PACK1X (PAC1X)

Drawing subroutines, PACKET format, PACK2X (PAC2X)

Drawing subroutines, PACKET format, PACKET

Drawing subroutines, PACKET format, TPACK (PACB)

Drawing subroutines, RASTER format, ASMESS

Drawing subroutines, RASTER format, DSHIP (SHIPSHO)

Drawing subroutines, RASTER format, MRASTR (RASTER)

Drawing subroutines, RASTER format, MSSPOS (POSDRAS)

Drawing subroutines, RASTER format, RASTER (RASTUR)

Drawing subroutines, RASTER format, RSTPOS (POSNRAS)

Drawing subroutines, RASTER format, RSTSIZ (SIZPRAS)

Drawing subroutines, RASTER format, SCRBTH

Drawing subroutines, RASTER format, SCRMES

Drawing subroutines, RASTER format, SELOPT (OPTION)

Drawing subroutines, RASTER format, SHIPX (SHIPSAT)

Drawing subroutines, RASTER format, TXTPOS (TEXPOS)

Drawing subroutines, RASTER format, TXTSIZ (TEXSIZ)

Drawing subroutines, SCORE format, SCRBTH

Drawing subroutines, SCORE format, SCRMES

Drawing subroutines, SCORE format, WAIT

EXPLOD, Working storage, RATEA

EXPLOD, Working storage, RATEB

EXPLOD, Working storage, RATEC

EXPLOD, Working storage, SATUS

EXPLOD, Working storage, VIBA

EXPLOD, Working storage, VIBB

EXPLOD, Working storage, VIBC

EXPLOD, Working storage, XACON

Hardware related subroutines, ACTGND (ZEREF)

Hardware related subroutines, CZERO (ZEGO)

Hardware related subroutines, DBNCE (ENPUT)

Hardware related subroutines, DEFLOK

Hardware related subroutines, DEL

Hardware related subroutines, DEL13

Hardware related subroutines, DEL20

Hardware related subroutines, DEL28

Hardware related subroutines, DEL33

Hardware related subroutines, DEL38

Hardware related subroutines, DPIO

Hardware related subroutines, DPRAM

Hardware related subroutines, DZERO (ZERO.DP)

Hardware related subroutines, FRWAIT (FRAM20)

Hardware related subroutines, INPUT

Hardware related subroutines, INT1Q

Hardware related subroutines, INT2Q (INTMID)

Hardware related subroutines, INT3Q

Hardware related subroutines, INTENS

Hardware related subroutines, INTMAX

Hardware related subroutines, INTPIA (INITPIA)

Hardware related subroutines, INTPSG (INITPSG)

Hardware related subroutines, JOYBIT (PBANG4)

Hardware related subroutines, JOYSTK (POTS4)

Hardware related subroutines, PSGLST (PSGLUP)

Hardware related subroutines, PSGMIR (PSGULP)

Hardware related subroutines, REQOUT

Hardware related subroutines, WAIT

Hardware related subroutines, WRPSG (PSG)

Hardware related subroutines, WRREG (PSGX)

Hardware related subroutines, ZERGND (ZEROIT)

Hardware related subroutines, ZERO (ZERO.)

Initialization subroutines, BCLR (CLRSOM)

Initialization subroutines, BLKFIL (FILL)

Initialization subroutines, CLR256

Initialization subroutines, CLR80 (NEGSOM)

Initialization subroutines, CLRBLK (CILL)

Initialization subroutines, CLREX (CLRMEM)

Initialization subroutines, INTALL (INITALL)

Initialization subroutines, INTMSC (INITMSC)

Initialization subroutines, INTPIA (INITPIA)

Initialization subroutines, INTPSG (INITPSG)

Initialization subroutines, INTREQ (IREQ)

Initialization subroutines, SCLR

Intensity control, INT1Q

Intensity control, INT2Q (INTMID)

Intensity control, INT3Q

Intensity control, INTENS

Intensity control, INTMAX

Interface adapter, Auxiliary control register

Interface adapter, Peripheral control register

Interface adapter, Port ‘A’ data register

Interface adapter, Port ‘A’ handshake controls (CA1 / 2)

Interface adapter, Port ‘B’ data register

Interface adapter, Port direction register

Interface adapter, interrupt enable register (IER)

Interface adapter, interrupt flag register (IFR)

Interface adapter, register access map

Interface adapter, shift register

Interface adapter, timer #1

Interface adapter, timer #2

Joystick enable, EPOT0 (DPOT0)

Joystick enable, EPOT1 (DPOT1)

Joystick enable, EPOT2 (DPOT2)

Joystick enable, EPOT3 (DPOT3)

Joystick related RAM, EPOT0 (DPOT0)

Joystick related RAM, EPOT1 (DPOT1)

Joystick related RAM, EPOT2 (DPOT2)

Joystick related RAM, EPOT3 (DPOT3)

Joystick related RAM, POT0

Joystick related RAM, POT1

Joystick related RAM, POT2

Joystick related RAM, POT3

Joystick related RAM, POTRES

Joystick related RAM, SJOY

Joystick related subroutines, JOYBIT (PBANG4)

Joystick related subroutines, JOYSTK (POTS4)

Joystick related subroutines, WAIT

MARKER format, DSHIP (SHIPSHO)

MARKER format, SHIPX (SHIPSAT)

Memory block subroutines, ADROT (DIFROT)

Memory block subroutines, APROT (POTATE)

Memory block subroutines, BCLR (CLRSOM)

Memory block subroutines, BDROT (DISROT)

Memory block subroutines, BLKFIL (FILL)

Memory block subroutines, BLKMOV (STFAUX)

Memory block subroutines, BLKMV1 (BAGAUX)

Memory block subroutines, CLR256

Memory block subroutines, CLR80 (NEGSOM)

Memory block subroutines, CLRBLK (GILL)

Memory block subroutines, CLREX (CLRMEM)

Memory block subroutines, DROT (DANROT)

Memory block subroutines, PROT (POTATA)

PACKET format, APACK

PACKET format, APROT (POTATE)

PACKET format, DASHPK (DASHY3)

PACKET format, DOTPCK (DOTPAK)

PACKET format, DPACK

PACKET format, LPACK (PACXX)

PACKET format, PACK1X (PAC1X)

PACKET format, PACK2X (PAC2X)

PACKET format, PACKET

PACKET format, PROT (POTATA)

PACKET format, TPACK (PACB)

PIA initialization, INTALL (INITALL)

PIA initialization, INTPIA (INITPIA)

PSG Sound mirror, REG0

PSG Sound mirror, REG1

PSG Sound mirror, REG2

PSG Sound mirror, REG3

PSG Sound mirror, REG4

PSG Sound mirror, REG5

PSG Sound mirror, REG6

PSG Sound mirror, REG7

PSG Sound mirror, REG8

PSG Sound mirror, REG9

PSG Sound mirror, REGA

PSG Sound mirror, REGB

PSG Sound mirror, REGC

PSG Sound mirror, REGD

PSG Sound mirror, REGE

PSG Working Storage, REQ0

PSG Working Storage, REQ1

PSG Working Storage, REQ2

PSG Working Storage, REQ3

PSG Working Storage, REQ4

PSG Working Storage, REQ5

PSG Working Storage, REQ6

PSG Working Storage, REQ7

PSG Working Storage, REQ8

PSG Working Storage, REQ9

PSG Working Storage, REQA

PSG Working Storage, REQB

PSG Working Storage, REQC

PSG Working Storage, REQD

PSG initialization, INTALL (INITALL)

PSG initialization, INTPSG (INITPSG)

Positioning subroutines, POSIT1

Positioning subroutines, POSIT2

Positioning subroutines, POSITB

Positioning subroutines, POSITD

Positioning subroutines, POSITN

Positioning subroutines, POSITX

Positioning subroutines, POSWID

Programmable Timers, D2TMR (DEKR3)

Programmable Timers, DECTMR (DEKR)

Programmable Timers, WAIT

Programmable Timers, Executive, XTMR0 (X0)

Programmable Timers, Executive, XTMR1 (X1)

Programmable Timers, Executive, XTMR2 (X2)

Programmable Timers, Executive, XTMR3 (X3)

Programmable Timers, Executive, XTMR4 (X4)

Programmable Timers, Executive, XTMR5 (X5)

Programmable Timers, Mine Storm, TMR1

Programmable Timers, Mine Storm, TMR2

Programmable Timers, Mine Storm, TMR3

Programmable Timers, Mine Storm TMR4

RAM initialization, BCLR (CLRSOM)

RAM initialization, BLKFIL (FILL)

RAM initialization, CLR256

RAM initialization, CLR80 (NEGSOM)

RAM initialization, CLRBLK (GILL)

RAM initialization, CLREX (CLRMEM)

RAM initialization, INTALL (INITALL)

RAM initialization, SCLR

RASTER format, ASMESS

RASTER format, DSHIP (SHIPSHO)

RASTER format, MRASTR (RASTER)

RASTER format, MSSPOS (POSDRAS)

RASTER format, RASTER (RASTUR)

RASTER format, RSTPOS (POSNRAS)

RASTER format, RSTSIZ (SIZPRAS)

RASTER format, SCRBTH

RASTER format, SCRMES

RASTER format, SELOPT (OPTION)

RASTER format, SHIPX (SHIPSAT)

RASTER format, TXTPOS (TEXPOS)

RASTER format, TXTSIZ (TEXSIZ)

REPLAY, Working storage, FADE

REPLAY, Working storage, FADEA

REPLAY, Working storage, FADEB

REPLAY, Working storage, FADEC

REPLAY, Working storage, NEWGEN

REPLAY, Working storage, RESTC

REPLAY, Working storage, TONEA

REPLAY, Working storage, TONEB

REPLAY, Working storage, TONEC

REPLAY, Working storage, TSTAT

REPLAY, Working storage, VIBE

REQ initialization, INTALL (INITALL)

REQ initialization, INTPSG (INITPSG)

REQ initialization, INTREQ (IREQ)

Random Number Generators, CONE

Random Number Generators, RAND3

Random Number Generators, RANDOM

Random Number Generators, RANPOS

Rotation subroutines, DIFFY format, ADROT (DIFROT)

Rotation subroutines, DIFFY format, BDROT (DISROT)

Rotation subroutines, DIFFY format, DROT (DANROT)

Rotation subroutines, DUFFY format, ADROT (DIFROT)

Rotation subroutines, DUFFY format, BDROT (DISROT)

Rotation subroutines, DUFFY format, DROT (DANROT)

Rotation subroutines, LINE format, ALNROT (ROTAR)

Rotation subroutines, LINE format, LNROT (ROTOR)

Rotation subroutines, LINE format, LROT90 (RATOR)

Rotation subroutines, LINE format, MLTY16

Rotation subroutines, LINE format, MLTY8

Rotation subroutines, PACKET format, APROT (POTATE)

Rotation subroutines, PACKET format, PROT (POTATA)

SELOPT, Working storage, FADE

SELOPT, Working storage, FADEA

SELOPT, Working storage, FADEB

SELOPT, Working storage, FADEC

SELOPT, Working storage, TONEA

SELOPT, Working storage, TONEB

SPLAY, Working storage, FADE

SPLAY, Working storage, FADEA

SPLAY, Working storage, FADEB

SPLAY, Working storage, FADEC

SPLAY, Working storage, NEWGEN

SPLAY, Working storage, RESTC

SPLAY, Working storage, TONEA

SPLAY, Working storage, TONEB

SPLAY, Working storage, TONEC

SPLAY, Working storage, TSTAT

SPLAY, Working storage, VIBE

Sine subroutines, LSINE (RSIN)

Sine subroutines, MSINE (RSINA)

Sine subroutines, SINCOS

Sine subroutines, SINE (SINGET)

Sound related subroutines, EXPLOD (AXE)

Sound related subroutines, INTPSG (INITPSG)

Sound related subroutines, INTREQ (IREQ)

Sound related subroutines, PSGLST (PSGLUP)

Sound related subroutines, PSGMIR (PSGULP)

Sound related subroutines, REQOUT

Sound related subroutines, SETAMP (LOUDIN)

Sound related subroutines, WRPSG (PSG)

Sound related subroutines, WRREG (PSGX)

TPLAY, Working storage, FADE

TPLAY, Working storage, FADEA

TPLAY, Working storage, FADEB

TPLAY, Working storage, FADEC

TPLAY, Working storage, NEWGEN

TPLAY, Working storage, RESTC

TPLAY, Working storage, TONEA

TPLAY, Working storage, TONEB

TPLAY, Working storage, TONEC

TPLAY, Working storage, TSTAT

TPLAY, Working storage, VIBE

Temporary Storage, Mine Storm, ETMP1

Temporary Storage, Mine Storm, ETMP2

Temporary Storage, Mine Storm, ETMP3

Temporary Storage, Mine Storm, ETMP4

Temporary Storage, Mine Storm, ETMP5

Temporary Storage, Mine Storm, ETMP6

Temporary Storage, Mine Storm, ETMP7

Temporary Storage, Mine Storm, ETMP8

Temporary Storage, Mine Storm, ETMP9

Temporary Storage, Mine Storm, ETMP10

Temporary Storage, Mine Storm, TEMP1

Temporary Storage, Mine Storm, TEMP2

Temporary Storage, Mine Storm, TEMP3

Temporary Storage, Mine Storm, TEMP4

Temporary Storage, Mine Storm, TEMP5

Temporary Storage, Mine Storm, TEMP6

Temporary Storage, Mine Storm, TEMP7

Temporary Storage, Mine Storm, TEMP8

Temporary Storage, Mine Storm, TEMP9

Temporary Storage, Mine Storm, TEMP10

Tune player subroutines, ASPLAY (SOPLAY)

Tune player subroutines, REPLAY

Tune player subroutines, REQOUT

Tune player subroutines, SPLAY

Tune player subroutines, TPLAY(YOPLAY)

Tune player subroutines, XPLAY

XPLAY, Working storage, FADE

XPLAY, Working storage, FADEA

XPLAY, Working storage, FADEB

XPLAY, Working storage, FADEC

XPLAY, Working storage, RESTC

XPLAY, Working storage, TONEA

XPLAY, Working storage, TONEB

XPLAY, Working storage, TONEC

XPLAY, Working storage, TSTAT